| 项目名称 Project Name | Integrated Petrochemical Complex Construction in Atyrau Region | 报告号 Report No. | CAPTCC-CT18017022-IR04 |
| --- | --- | --- | --- |
| 客户 Client | Kazakhstan Petrochemical Industries Inc LLP | 客户订单号 Client P.O. No. | CT18017022 |
| 检验通知号 Reference No. | / | 检验员 Inspector | Zhangliu |
| 制造商 Vendor | Changzhou Heyu Environmental Protection Technology Co., Ltd. | 检验地址 Inspection Location | Changzhou City, Jiangsu Province |
| 分包商 Sub-Vendor | / | 检验日期 Visit Date(s) | 14th Dec. 2019 |

| 本次检验参与人员 THE PARTICIPANTS OF THIS VISIT |
| --- |
| 姓名 NAME | 公司 COMPANY | 代表方 REPRESENTING | 联系方式 CONTACT NO. |
| Zhangliu | CNCEC | TCC | 18768063866 |
| LiangJianmin | Heyu | Heyu | 15801539040 |

| 本次检验产品 MATERIAL/ SUBJECT OF INSPECTION | 编号 Item No. | 订单数量 QTY as per P/O | 所检数量 QTY offered for inspection |
| --- | --- | --- | --- |
| Fan stack | / | 4 sets | 4 sets |

| 适用文件 参考附件 REFERENCE DOCUMENTATION Refer to attachments instead |
| --- |
| 标题 Title | 文件编号 Reference No | 版本 Rev. | 批准状态 Approval status | 批准人 Approved by | 日期 Date |
| ITP | QZKPI-7620-WS-PO-27.08A-Q02-001 | 1 |  |  |  |
| Drawing | D9140H4270-1 | B |  |  |  |
| Drawing | D9140H4270-2 | A |  |  |  |
| Drawing | D9140H4270-3 | A |  |  |  |

| ITP 相关 REFERENCE ITP |
| --- |
| 序号 S/N | 设备名称 Equipment/material | 检验项目 Inspection Activity (detail according to scope /standard/etc.) | 检验等级 Inspection Level H/W/SW/R | 相关文件 Relevant document |
| 1 | Fan Stack | Identification of material | R | MFR’S Spec. |
| 2 | Fan Stack | Visual check of fan stacks | R | / |
| 3 | Fan Stack | Check of dimension and thickness (random) | W | See drawing |
| 4 | Fan Stack | Check of corrosion protection/surface treatment (random) | W | MFR’S Spec. |
| 5 | Fan Stack | Trial assembly of one fan stack incl. Roundness check | W | See drawing |

| 检验结果 INSPECTION RESULT |
| --- |
| 合格 Satisfactory (without comments) | 假释 Satisfactory with comments (Any of trailing punch or non-conformity items is still open) | 不合格 Not Satisfactory (NCR raised during the inspection) |
| 检验概述： SUMMARY Reviewed MTCs of raw material and found for the was not satisfied with specification, unacceptable, Visual inspection was carried out, there was no defect or damage found, acceptable. Dimension inspection was performed, all measured values were within tolerance of drawing and GB1804-79, acceptable. Checked the corrosion protection and surface treatment and no defect was found, acceptable. Trial assembly inspection was executed, checked the roundness, height, orientation of maintenance door and technical integrity, found the viewing window did not opening, the length of bolt used on the lower side of maintenance door was too long and the handle missing installation on maintenance door, needed to modify before packing. |
| 不符合项 Open Non Conformities | 是，详见不符合项表格 Yes, details in non-conformities | 无 No |
| 尾项清单 Open Punch List Items | 是,详见尾项情单表格 Yes, details in punch list | 无 No |
| 检验员签名 Inspector signature | Zhangliu | 报告日期 Inspection report date | 15th Dec. 2019 |

| 不符合项 参考附件 NON CONFORMITIES Refer to attachments instead |
| --- |
| 项目 Item | 描述 Description | 状态 Status | 提出日期/报告号 Raised on/ Report # | 关闭日期/报告号 Closed on/ Report # | 备注 Comments |
| / | / | / | / | / | / | / | / |

| 尾项清单 参考附件 PUNCH LIST Refer to attachments instead |
| --- |
| 项目 Item | 描述 Description | 状态 Status | 提出日期/报告号 Raised on/ Report # | 关闭日期/报告号 Closed on/ Report # | 备注 Comments |
| 4 sets fan stacks | MTCs of unsaturated polyester resin not satisfied with specification. | Open | 14th Dec. 2019 | IR04 |  |  | MTCs needed to submit for reviewing before shipping. |
| 4 sets fan stacks | Opening of viewing window did not cutting as drawing. | Open | 14th Dec. 2019 | IR04 |  |  | Opening should be cut before packing. |
| 4 sets fan stacks | The length of bolt used on the lower side of maintenance door was too long, it was inconvenient and not safe to use | Open | 14th Dec. 2019 | IR04 |  |  | Heyu needed to purchase bolts of the same specification with appropriate length. |
| 4 sets fan stacks | Handle missing installation on maintenance door | Open | 14th Dec. 2019 | IR04 |  |  | The handle should be installation before packing |

| 检验项目 THE ITEMS OF INSPECTION |
| --- |
| 预检会 Pre-inspection Meeting |  | 材料检验 Material Inspection |  | 数量检查 Quantity Check |  |
| 外观检验 Visual Inspection |  | 尺寸检验 Dimension Inspection |  | 试验见证 Test Witness |  |
| 防腐检验 Coating Inspection |  | 文件审核 Documents Review |  | 包装和标识检验 Packing & Marking Inspection |  |
| 装车/船检验 Loading Inspection |  | 其他 Others | Trial assembly inspection |

检验详述 INSPECTION DETAILS

检验活动如下： Description of the inspections carried out: 材料检验MATERIALS INSPECTION NA 数量检查QUANTITY CHECK Quantity inspection was carried out, there were 72pcs section completed (18pcs of each set, including 1pcs of repairing door, 4sets in total), they were satisfied with PO, acceptable. 外观检验VISUAL INSPECTION Randomly checked the surface of fan stack, there was no crack, deformation or delamination found, acceptable. Opening of viewing window did not cutting as drawing, the inspector required Heyu to modify ASAP. The length of bolt used on the lower side of maintenance door was too long, it was inconvenient and not safe to use, to be modify. Handle on maintenance door was found missing installation, it was not satisfied with drawing, unacceptable. 尺寸检验DIMENTION INSPECTION Roundness inspection was carried out, 18points were checked for inside diameter, detail please refer to table below. NO. 1 2 3 4 5 6 7 8 9 Average Required (mm) 9205~9240 / Measured (mm) 9214 9228 9238 9238 9235 9210 9205 9206 9207 9220 NO. 1 2 3 4 5 6 7 8 9 Average Required (mm) 9205~9240 / Measured (mm) 9214 9231 9240 9241 9234 9220 9208 9208 9201 9221.4 Checked the height were 4269~4272mm (required was 4270mm), acceptable. The size of maintenance door inspection was performed, all the measured values were satisfied with drawing, acceptable. 防腐检验COATING INSPECTION Randomly checked the appearance quality of coating and no defect was found, acceptable. 功能试验FUNCTIONAL AND PERFORMANCE TEST NA 特殊程序SPECIAL PROCESSES NA 包装和标识检验PACKING AND MARKING INSPECTION Checked packing form of the section, there were 12 sections packed as one package, the soft foam and wooden plate used for separation between section and packing bracket, acceptable. Inspector required Heyu to pack outside with plastic sheeting for each package to keep out dust and rain, acceptable according to QZKPI-0000-IA-SPC-0007_A00. Three straps were used to prevent sloshing that may cause damage during transportation, acceptable. 装车/装船检验 LOADING INSPECTION NA 文件审查 DOCUMENTATION REVIEW Reviewed MTCs of raw material, found the MTC of unsaturated polyester resin was not satisfied with requirement of specification, Heyu needed to resubmit English revision for reviewing before shipping. Reviewed the certificates of measuring tools used for this visiting and found they were within the validity period of the verification, acceptable. 放行/不符合项 RELEASE/NON-COMFORMANCE MTCs of unsaturated polyester resin not satisfied with specification. Opening of viewing window did not cutting as drawing. The length of bolt used on the lower side of maintenance door was too long, it was inconvenient and not safe to use. Handle missing installation on maintenance door, to be modify. 健康安全/HEALTH AND SAFE There was not any safety equipment provided by vendor. 附件/ATTACHMENTS ATT 01 CAPTCC-CT18017022-IR04-Photos ATT 02 MTCs of Raw material ATT 03 Verification certificates 下一次检验/NEXT VISIT NA

| 附件 ATTACHMENT |
| --- |
| 序号 Item | 附件名称 Attachment name | 描述 Description |
| 1 | CAPTCC-CT18017022-IR04-Photos | Inspection Photos |
| 2 | MTCs of Raw material | MTCs of Raw material |
| 3 | Verification certificates | Verification certificates |

结束 End of Report